RGB Led Fader using AVR Assembly.

Danh Pham
Michael Harper
Samuel Bowker

COSC-2325-001

12/15/2016

Introduction:

Our project was to control a piece of hardware in a precise, time-sensitive manner by using an Arduino. The Arduino is a microcontroller that can be programmed at a very low level using assembly, directly manipulating the input and out from its I/O ports. Doing this allows us to directly interact with a variety of digital devices’ mechanisms. We used this to control the brightness of an RGB LED, allowing us to set it to light up any color we wished with buttons controlling it.

Micro controller platform details:

The Arduino Uno has an ATmega328P processor, and runs at a clock speed of 16 MHz. It has 32 KB of onboard flash memory, 0.5 KB of which is used by the boot loader. It has an operating voltage of 5V, and can supply 20 mA to each of its 14 digital I/O pins.

Test device details:

Our test device consists of an Arduino Uno micro controller, a 3-pin RGB LED, and 6 push-button switches. The LED is wired to three pins on the Arduino that are capable of pulse width modulation. The buttons are connected to six more I/O pins on the Arduino so that it can accept input from them.

Development tools:

The program was written in AVR assembly. A Makefile was used to build the ELF executable with avr-gcc, and to create and load the .hex file with avrdude.

The experiment:

Our experiment was to get pulse width modulation working to control the brightness of an RGB LED. We then used push buttons to vary the signal created by the PWM, allowing us to control the brightness with the LED still on.

Conclusions:

Using assembly to program has its benefits and downsides. By using assembly, we were able to much more directly and precisely control the timing of the program. This allowed us to use pulse width modulation to vary the brightness of the led despite only being able to output a digital signal to it. The main downside of using assembly, is the complexity of it. The task we accomplish took more than an order of magnitude more lines of code to accomplish in assembly, then it would have in a higher level language like C++. The precision assembly gives come from the precision put into writing the code.

Project code listing.

src/
src/Makefile
src/config.inc
src/timer.S
src/aBrightness.S
src/delay.S
src/include
src/include/AVRMakeLinux.mak
src/include/AVRMakeWin.mak
src/include/AVRMakefile.mak
src/include/AVRSpecialRegs.inc
src/include/AVRMakeMac.mak
src/include/AVRBuildRules.mak
report/
report/report.txt
README.md
images/
images/Diagram.png